## Slide 1: Accessing Drone Data — STAC + COG / COPC
What is it — why should we care
Vincent Le Falher · ForestGEO/STRI Gamboa · April 2026

## Slide 2: The problem in one number
BCI whole-island RGB drone mosaic = 50 GB per date — 17+ dates available
Old workflow:
• Download the whole file *(hours)*
• Open it locally *(runs out of RAM)*
• Look at 0.01 % of it
• Repeat for every date
This does not scale — the BCI archive alone is over 750 GB.
The full COG/COPC collection across all sites is > 13 TB and counting.

## Slide 3: Where do these formats come from?
Format | Born | Who | Status
COG | 2016 | Open-source geo community (Planet Labs, GDAL team, AWS) | OGC Community Standard since 2023
COPC | 2021 | Hobu Inc. + PDAL contributors | Open spec, built on LAZ/LASzip
STAC | 2017 | Radiant Earth + cloud providers (AWS, Microsoft, Google) | OGC Community Standard since 2021
Why trust them?
• GDAL supports all three → works in every GIS tool you already use
• Adopted by NASA Earthdata, ESA Copernicus, Microsoft Planetary Computer, Google Earth Engine
• Open specifications — no vendor lock-in, no licence fees

## Slide 4: What if the file stayed on the server?
Like streaming a movie: you don't download the whole film before watching the first frame.
`
Your laptop ──► "give me tiles for this bounding box" ──► server
◄── ~800 KB ◄──
`
You read ~800 KB from a 50 GB file.
That is exactly what COG and COPC enable.

## Slide 5: COG — Cloud Optimized GeoTIFF
A regular GeoTIFF reorganised so that:
Feature | What it means
Internal tiling | Data split into small spatial blocks
Overviews baked in | Zoom-out views pre-computed at multiple resolutions
HTTP Range requests | Client asks only for the bytes it needs
Result: open a 50 GB file, read a 512 × 512 chip → ~800 KB transferred
Works in QGIS, R (terra), Python (rasterio), ArcGIS — any GDAL-based tool.

## Slide 6: COPC — Cloud Optimized Point Cloud
Same idea, but for LiDAR / photogrammetry point clouds.
 | Regular LAZ | COPC
Access pattern | Download everything, then filter | Spatial index baked in — stream only needed points
Per-tree extraction | Download full flight first | Stream bounding box directly
Pan & zoom over HTTP | Not possible | Native
Works in PDAL, Python, QGIS — same GDAL-based ecosystem.

## Slide 7: STAC — SpatioTemporal Asset Catalog
COG/COPC without a catalogue = a hard drive full of files you can't search.
STAC adds structured, queryable metadata for every file:
• Date and time of acquisition
• Bounding box / footprint
• Collection name, sensor, resolution
• Direct link to the COG or COPC asset
Query by date, place, collection — results in under a second.
No login, no download, no local storage needed.

## Slide 8: Our setup at BCI
Layer | What
STAC catalogue | All BCI collections indexed and queryable
COG files | Hosted on Etienne's NAS — HTTP range requests enabled
Collections | bciwhole (17+ dates), 50ha plot, research plots, tower sites, …
Total archive | > 13 TB COG + COPC across all sites
BCI whole-island collection:
• 17+ dates spanning 2024–2025
• ~47–54 GB per date
• > 750 GB total — streamed on demand, never downloaded in full

## Slide 9: Why downloading is not an option
Gamboa network speeds (measured April 2026):
Location | Speed | Time to download one 50 GB COG
SI-internal Gamboa Lab | 19.4 Mbps | ~6h
STRI Camino de Cruces | 25.1 Mbps | ~4h 50m
GAMBOA RF Las Jacarandas | 36.7 Mbps | ~3h 20m
GAMBOA RF Camino de Cruces | 4.7 Mbps | ~24h
With COG streaming → same query, any network: ~2 seconds

## Slide 10: Why this matters for your research
Before | Now
Email someone for a file | Query the catalogue yourself
Download 50 GB, run out of disk | Stream only the patch you need
"I don't know what dates are available" | Search by date range in one step
QGIS crashes opening the full mosaic | Load as COG — only fetches visible tiles
Wait hours on Gamboa wifi | 2-second chip, any connection
Drone data becomes as easy to access as Sentinel or Landsat.

## Slide 11: This week
When | What
Today (10 min) | This talk — concepts
Thu 13:00–14:00 | Live demo: BCI COG chips, vegetation indices, QGIS temporal animation
Thu 14:00–15:00 | Hands-on: Python / R / QGIS — you run the code
Catalogue: kanopia.org/stac-fastapi-pgstac/api/v1/pgstac/
Workshop access — User: panama · Password: panama123
Questions? Let's go.